## Slide 1
Chapter 3
Data and Signals
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.

## Slide 2
To be transmitted, data must be transformed to electromagnetic signals.
Note

## Slide 3
3-1 ANALOG AND DIGITAL
Data can be analog or digital. The term analog data refers to information that is continuous; digital data refers to information that has discrete states. Analog data take on continuous values. Digital data take on discrete values.
Analog and Digital Data Analog and Digital Signals Periodic and Nonperiodic Signals
Topics discussed in this section:

## Slide 4
Note
Data can be analog or digital. Analog data are continuous and take continuous values.
Digital data have discrete states and take discrete values.

## Slide 5
Signals can be analog or digital. Analog signals can have an infinite number of values in a range; digital signals can have only a limited number of values.
Note

## Slide 6
Figure 3.1 Comparison of analog and digital signals

## Slide 7
In data communications, we commonly use periodic analog signals and nonperiodic digital signals.
Note

## Slide 8
3-2 PERIODIC ANALOG SIGNALS
Periodic analog signals can be classified as simple or composite. A simple periodic analog signal, a sine wave, cannot be decomposed into simpler signals. A composite
periodic analog signal is composed of multiple sine waves.
Sine Wave Wavelength Time and Frequency Domain Composite Signals
Bandwidth
Topics discussed in this section:

## Slide 9
Figure 3.2 A sine wave

## Slide 10: Characteristics of sine wave
Amplitude
Phase
frequency

## Slide 11
Figure 3.3 Two signals with the same phase and frequency, but different amplitudes

## Slide 12
Frequency and period are the inverse of each other.
Note

## Slide 13
Figure 3.4 Two signals with the same amplitude and phase, but different frequencies

## Slide 14
Table 3.1 Units of period and frequency

## Slide 15
Frequency is the rate of change with respect to time. Change in a short span of time
means high frequency. Change over a long span of time means low frequency.
Note

## Slide 16
If a signal does not change at all, its frequency is zero.
If a signal changes instantaneously, its frequency is infinite.
Note

## Slide 17
Phase describes the position of the waveform relative to time 0.
Note

## Slide 18
Figure 3.5 Three sine waves with the same amplitude and frequency, but different phases

## Slide 19
Figure 3.7 The time-domain and frequency-domain plots of a sine wave

## Slide 20
A complete sine wave in the time domain can be represented by one single spike in the frequency domain.
Note

## Slide 21
Figure 3.8 The time domain and frequency domain of three sine waves

## Slide 22
A single-frequency sine wave is not useful in data communications;
we need to send a composite signal, a signal made of many simple sine waves.
Note

## Slide 23
The bandwidth of a composite signal is the difference between the
highest and the lowest frequencies contained in that signal.
Note

## Slide 24
Figure 3.12 The bandwidth of periodic and nonperiodic composite signals

## Slide 25
Figure 3.14 The bandwidth for Example 3.11

## Slide 26
3-3 DIGITAL SIGNALS
In addition to being represented by an analog signal, information can also be represented by a digital signal. For example, a 1 can be encoded as a positive voltage and a 0 as zero voltage. A digital signal can have more than two levels. In this case, we can send more than 1 bit for each level.
Bit Rate Bit Length
Topics discussed in this section:

## Slide 27
Bit rate
  Number of bits sent in one second.
  The term bit rate is used instead of frequency for digital signals.
Bit length
  Is the distance one bit occupies on transmission medium.

## Slide 28
Figure 3.16 Two digital signals: one with two signal levels and the other with four signal levels

## Slide 29
3-4 TRANSMISSION IMPAIRMENT
Signals travel through transmission media, which are not perfect. The imperfection causes signal impairment. This means that the signal at the beginning of the medium is not the same as the signal at the end of the medium. What is sent is not what is received. Three causes of impairment are attenuation, distortion, and noise.
Attenuation Distortion Noise
Topics discussed in this section:

## Slide 30
Figure 3.25 Causes of impairment

## Slide 31
Figure 3.26 Attenuation

## Slide 32
Figure 3.28 Distortion

## Slide 33
Figure 3.29 Noise

## Slide 34
3-6 PERFORMANCE
One important issue in networking is the performance of the network—how good is it? We discuss quality of service, an overall measurement of network performance, in greater detail in Chapter 24. In this section, we introduce terms that we need for future chapters.
Bandwidth Throughput Latency (Delay)
Bandwidth-Delay Product
Topics discussed in this section:

## Slide 35
In networking, we use the term bandwidth in two contexts.
❏ The first, bandwidth in hertz, refers to the range of frequencies in a composite signal or the range of frequencies that a channel can pass.
❏ The second, bandwidth in bits per second, refers to the speed of bit transmission in a channel or link.
Note

## Slide 36
Throughput
  Is define as ”how fast we can actually send data”
Delay
  How long it takes for an entire message to completely arrive at the destination from the time the first bit is sent out from the source,

## Slide 37
Figure 3.31 Filling the link with bits for case 1

## Slide 38
The bandwidth-delay product defines the number of bits that can fill the link.
Note