## Slide 1
Chapter 1
Introduction
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.

## Slide 2
1-1 DATA COMMUNICATIONS
The term telecommunication means communication at a distance. The word data refers to information presented in whatever form is agreed upon by the parties creating and using the data. Data communications are the exchange of data between two devices via some form of transmission medium such as a wire cable.
Components
Data Representation Data Flow
Topics discussed in this section:

## Slide 3
Figure 1.1 Five components of data communication

## Slide 4: Data Representation
Text, numbers, images, audio, and video are different forms of Data Representation.
Text
In data communications, text is represented as a bit pattern, a sequence of bits.
Different sets of bit patterns have been designed to represent text symbols. Each set is called a code, and the process of representing symbols is called coding i.e ASCII made by ANSI, Unicode

## Slide 5: Data Representation cont..
Numbers are also represented by using bit patterns. However , a code such as ASCII is not used to represent numbers; the numbers is directly converted to a binary number.
Images today are also represented by bit patterns but an image is divided in to a matrix of pixels.
Audio is a representation of sound. It is a continuous , not discrete.
Video can be produced either as a continuous entity or it can be a combination of images.

## Slide 6
Figure 1.2 Data flow (simplex, half-duplex, and full-duplex)

## Slide 7
1-2 NETWORKS
A network is a set of devices (often referred to as nodes) connected by communication links. A node can be a computer, printer, or any other device capable of sending and/or receiving data generated by other nodes on the network.
Distributed Processing
Network Criteria Physical Structures Network Models Categories of Networks Interconnection of Networks: Internetwork
Topics discussed in this section:

## Slide 8: Network
A network is a set of devices (often referred to as nodes) connected by communication links.
Distributed Processing
  Most Networks use distributed processing, in which a task is divided among multiple computers

## Slide 9: Network Criteria
A network must be able to meet a certain number of criteria. The most important of these are
Performance
Reliability
Security

## Slide 10: Physical Structures
Type of Connection
Physical Topology
Point-to-point connection

## Slide 11: Physical Structures Cont..
Multipoint Connection

## Slide 12: Physical topology
Topology refers to the physical or logical arrangement of a network.

## Slide 13: Mesh Topology
In a mesh topology, every device has a dedicated point to point link to every other device.

## Slide 14: Star Topology
In a star topology, each device has a dedicated point to point link only to a central controller.

## Slide 15: Bus Topology
A bus topology is a multipoint topology in which one long cable acts as a backbone to link all the devices in the network.

## Slide 16: Ring topology
In a ring topology, each device has a dedicated point to point connection only with two devices on either side of it.

## Slide 17: Categories of Networks

## Slide 18: Local Area Network
A local area network is usually privately owned and links the devices in a single office, building, or campus.

## Slide 19: Metropolitan Area Network
A MAN is a data communication system covering an area the size of a town or city.

## Slide 20: Wide Area Network
A WAN is a data communication system spanning states, countries, or the whole world.

## Slide 21: WAN Implementation
Traditionally, WANs have been implemented using one of two technologies:
  Circuit Switching
  Packet Switching
Circuit Switching
In a circuit switching network, a dedicated communication path is established between two stations through the nodes of the network. Telephone network is a example of Circuit switching.
Packet Switching
In packet Switching it is not necessary to dedicate communication path between two stations. Data are sent out in a sequence of small chunks, called packets.

## Slide 22: WAN Implementation cont…
Frame Relay
Frame Relay is also a packet switching technique with variable length packets develop to take the advantages of high data rates and low error rates of current Transmission Systems.
ATM
Asynchronous transfer mode, sometimes referred to as cell relay, is a culmination of developments in circuit switching and packet switching. ATM technology uses a fixed size packet called a cell.

## Slide 23: Protocols and Standards
Protocol
A protocol is a set of rules that governs data communication;
The key elements of a protocol are Syntax, Semantics and Timing.
Syntax
Syntax refers to the structure or format of the data. For example, a simple protocol might expect the first 8 bits of data to be the address of the sender, the second 8 bits to be the address of the receiver, and the rest of the stream to the message itself.
Semantics
Semantics refers to the meaning of each section of bits. For example, does an address identify the route to be taken or the final destination of the message?
Timing
Timing refers to two characteristics: when data should be sent and how fast they can be sent.

## Slide 24: Protocols and Standards
Standards
Standards are necessary to ensure that products from different manufactures can work together as expected.
Data communication Standards fall in to two categories: de facto and de jure
De facto
Meaning by fact, standards that have not been approved by an organized body but have been adopted as standards through widespread, Often established originally by manufactures that seek to define the functionality of a new product or technology.
De jure
Those that have been legislated by an officially recognized body.

## Slide 25: Standards Organizations
International Organization for Standardization (ISO)
International Telecommunication Union-Telecommunication Standards (ITU-T)
American National Standards Institute (ANSI)
Institute of Electrical and Electronics Engineers (IEEE)
Electronic Industries Association (EIA)

## Slide 26
Chapter 2
Network Models
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.

## Slide 27
2-1 LAYERED TASKS
We use the concept of layers in our daily life. As an example, let us consider two friends who communicate through postal mail. The process of sending a letter to a friend would be complex if there were no services available from the post office.
Sender, Receiver, and Carrier Hierarchy
Topics discussed in this section:

## Slide 28
Figure 2.1 Tasks involved in sending a letter

## Slide 29
2-2 THE OSI MODEL
Established in 1947, the International Standards Organization (ISO) is a multinational body dedicated to worldwide agreement on international standards. An ISO standard that covers all aspects of network communications is the Open Systems Interconnection (OSI) model. It was first introduced in the late 1970s.
Layered Architecture Peer-to-Peer Processes
Encapsulation
Topics discussed in this section:

## Slide 30
ISO is the organization. OSI is the model.
Note

## Slide 31
Figure 2.2 Seven layers of the OSI model

## Slide 32
Figure 2.3 The interaction between layers in the OSI model

## Slide 33
Figure 2.4 An exchange using the OSI model

## Slide 34
2-3 LAYERS IN THE OSI MODEL
In this section we briefly describe the functions of each layer in the OSI model.
Physical Layer Data Link Layer
Network Layer
Transport Layer
Session Layer
Presentation Layer
Application Layer
Topics discussed in this section:

## Slide 35
Figure 2.5 Physical layer

## Slide 36
The physical layer is responsible for movements of
individual bits from one hop (node) to the next.
Note

## Slide 37
Duties of Physical Layer
Physical Characteristics of interfaces and medium
Representation of bits
Data rate
Synchronization of bits
Line configuration
Physical topology
Transmission modes

## Slide 38
Figure 2.6 Data link layer

## Slide 39
The data link layer is responsible for moving frames from one hop (node) to the next.
Note

## Slide 40
Figure 2.7 Hop-to-hop delivery

## Slide 41
Duties of Data Link Layer
Framing
Physical addressing
Flow control
Error Control
Access Control

## Slide 42
Figure 2.8 Network layer

## Slide 43
The network layer is responsible for the delivery of individual packets from
the source host to the destination host.
Note

## Slide 44
Figure 2.9 Source-to-destination delivery

## Slide 45
Duties of Network Layer
Logical Addresssing
Routing

## Slide 46
Figure 2.10 Transport layer

## Slide 47
The transport layer is responsible for the delivery of a message from one process to another.
Note

## Slide 48
Figure 2.11 Reliable process-to-process delivery of a message

## Slide 49
Duties of Transport Layer
Service point addressing
Segmentation and reassembly
Connection control
Flow control
Error control

## Slide 50
Figure 2.12 Session layer

## Slide 51
The session layer is responsible for dialog control and synchronization.
Note

## Slide 52
Duties of Session Layer
Dialog Control
Synchronization points

## Slide 53
Figure 2.13 Presentation layer

## Slide 54
The presentation layer is responsible for translation, compression, and encryption.
Note

## Slide 55
Duties of Presentation Layer
Translation
Encryption
Compression

## Slide 56
Figure 2.14 Application layer

## Slide 57
The application layer is responsible for providing services to the user.
Note

## Slide 58
Duties of Application Layer
Network virtual terminal
File transfer, access and management
Mail services
Directory services

## Slide 59
Figure 2.15 Summary of layers

## Slide 60
2-4 TCP/IP PROTOCOL SUITE
The layers in the TCP/IP protocol suite do not exactly match those in the OSI model. The original TCP/IP protocol suite was defined as having four layers: host-to-network, internet, transport, and application. However, when TCP/IP is compared to OSI, we can say that the TCP/IP protocol suite is made of five layers: physical, data link, network, transport, and application.
Physical and Data Link Layers Network Layer Transport Layer
Application Layer
Topics discussed in this section:

## Slide 61
Figure 2.16 TCP/IP and OSI model

## Slide 62
2-5 ADDRESSING
Four levels of addresses are used in an internet employing the TCP/IP protocols: physical, logical, port, and specific.
Physical Addresses Logical Addresses Port Addresses Specific Addresses
Topics discussed in this section:

## Slide 63
Figure 2.17 Addresses in TCP/IP

## Slide 64
Figure 2.18 Relationship of layers and addresses in TCP/IP

## Slide 65
In Figure 2.19 a node with physical address 10 sends a frame to a node with physical address 87. The two nodes are connected by a link (bus topology LAN). As the figure shows, the computer with physical address 10 is the sender, and the computer with physical address 87 is the receiver.
Example 2.1

## Slide 66
Figure 2.19 Physical addresses

## Slide 67
As we will see in Chapter 13, most local-area networks use a 48-bit (6-byte) physical address written as 12 hexadecimal digits; every byte (2 hexadecimal digits) is separated by a colon, as shown below:
Example 2.2
07:01:02:01:2C:4B
A 6-byte (12 hexadecimal digits) physical address.

## Slide 68
Figure 2.20 shows a part of an internet with two routers connecting three LANs. Each device (computer or router) has a pair of addresses (logical and physical) for each connection. In this case, each computer is connected to only one link and therefore has only one pair of addresses. Each router, however, is connected to three networks (only two are shown in the figure). So each router has three pairs of addresses, one for each connection.
Example 2.3

## Slide 69
Figure 2.20 IP addresses

## Slide 70
Figure 2.21 shows two computers communicating via the Internet. The sending computer is running three processes at this time with port addresses a, b, and c. The receiving computer is running two processes at this time with port addresses j and k. Process a in the sending computer needs to communicate with process j in the receiving computer. Note that although physical addresses change from hop to hop, logical and port addresses remain the same from the source to destination.
Example 2.4

## Slide 71
Figure 2.21 Port addresses

## Slide 72
The physical addresses will change from hop to hop,
but the logical addresses usually remain the same.
Note

## Slide 73
Example 2.5
As we will see in Chapter 23, a port address is a 16-bit address represented by one decimal number as shown.
753
A 16-bit port address represented as one single number.

## Slide 74
The physical addresses change from hop to hop,
but the logical and port addresses usually remain the same.
Note